## Slide 1: Iot plant monitoring system

## Slide 2: Purpose of the project
Implement an autonomous system for the monitoring of plant.
Various sensors to collect measurements from the plant.
Autonomous watering.
MQTT communication.
Raspberry Pi broker.
E-mail notifications.
Real-time measurements charts.

## Slide 3: System architecture

## Slide 4: System architecture

## Slide 5: Hardware – esp32
Built-in WiFi and Bluetooth.
Greater memory size compared to Arduino Uno.
Increased number of pins.

## Slide 6: HARDWARE - SENSORS Soil moisture
Water level
Measures how wet the soil is.
Used to determine when to activate the pump.
Measures how much water remains.

## Slide 7: HARDWARE - SENSORS Air HUMIDITY AND TEMPERATURE
PHOTORESISTOR
Measures the light level near the plant.

## Slide 8: HARDWARE – Controller and pump L293d motor driver
5v water pump
Sits in water
Triggers based on soil moisture levels.
Can control up to 2 pumps at once.

## Slide 9: MQTT COMMUNICATION
Mosquitto broker running on a Rapsberry Pi:
Collects messages from ESP32.
Web server subscribes to topics.
A topic for each measurement:
  /iot/moisture
  /iot/water
  /iot/light
  /iot/temperature
  /iot/humidity

## Slide 10: Moisture level real-time chart

## Slide 11: Water level real-time chart

## Slide 12: LIGHT LEVEL REAL-TIME CHART

## Slide 13: E-MAIL NOTIFICATION
Anomalies can be detected in the measurements, i.e.:
Low water level in the reserve.
Dangerous values for temperature/light…
In case this happens, the user is notified vie e-mail.

## Slide 14: Thank you for the attention!